## Slide 1: Rainwater Harvesting
Janie Harris
Extension Specialist
Housing and Home Environment
Texas AgriLife Extension Service

## Slide 2: Efficient Water Use is Critical
Limited water supply
Growing population
Rainwater catchment is a source of water
Water will not always be inexpensive

## Slide 3
Increased Demand for a Decreasing Supply
Rising Environmental & Economic Costs
Rainwater’s Purity
Conservation – Saving Your Water!
Reduce Runoff – Crucial in Cities
Droughts have Increased Need & Awareness
Water for Areas w/o Groundwater or Service
Why Collect Rainwater?

## Slide 4
Cisterns - The only source of water for many before electricity and well drillers
Notes: Cisterns have been around for a long time. A cistern is a primitive rainwater harvesting system. Today’s systems can be designed to capture and store water on land or in a storage tank. The parts of a rainwater harvesting system are:
Catchment – the area where the rain first falls
Conveyance system – directs water from catchment to storage containers
Storage
Distribution
Today, we will see an overview of rainwater harvesting. If you want more detailed information, go to the Rainwater Harvesting Guide published by TCE, B-6153.

## Slide 5
Increased Impervious Area from pavement & roofs
Notes: Storm water runoff is a real problem for may communities. It is sometimes a problem for households. The hard surfaces in cities and around homes has increased. By preventing the runoff from roofs, parks, etc. we can reduce the storm water runoff problem.

## Slide 6
Value of Rainwater
Low pH 6.0 to 7.0
High quality water
Makes You Conservation Minded
Free
Notes: Read slide

## Slide 7
Attract and provide water for wildlife, pets, birds and butterflies
Landscape irrigation, house plants
In home use – laundry, bath/shower, drinking, cleaning, etc.
Rainwater Uses
Notes: Rainwater can be used for anything that municipal or well water can be used for. It typically has fewer minerals in it which makes it good for your plants. If you use it for drinking water in the home, it should be treated.

## Slide 8
How to Catch Rainwater
* Roof – Sloped Tin is best but any will work
* .6 gallons per square foot roof
* 2,000 sq. foot roof X 1" rain = 1,200 gal. water
* 1,200 gal. X 20" rainfall per year= 24,000 gal/yr.
* 12” rain yields 14,400 gals./yr.
* 6” rain yields 7,200 gals./yr.
Notes: Homeowners can collect, store and use about 600 gallons per 1000 square feet of roof and pavement areas for each inch of rainfall. Do the calculations based on your annual rainfall. Lubbock has average rainfall of 18” per year. 18 X 1,200 gal. = 21,600 gallons captured. With water saving landscape plants and efficient irrigation, this should be enough water along with the falling rain for the landscape. Remember that landscapes are not watered year round.

## Slide 9
Gutters - Nothing special
Roof washers - removes trash, debris & dust
Gutters and Roof Washers

## Slide 10
Screens to Keep Out Trash & Mosquitoes

## Slide 11
Durable and water tight – material
Opaque
Size – depends on how much you will collect and need and where the water will be used
Cost - $ .30 - 1.25 per gallon collected
Cisterns or Tanks for Storage of Water

## Slide 12: Small Rain Barrels

## Slide 13: Simple Rain Barrel w/Gutter

## Slide 14: Selection – Size, Color, Shape

## Slide 15
Gate valve and facets
The Other Parts

## Slide 16
The clear plastic hose allows water to rise to the level the water is inside the tank
Water Gauge

## Slide 17
Overflow allows water to run out of tank when full rather than backing up into the gutter of this Rain Barn
Overflow Pipe
Notes: One other feature that is illustrated on this picture is the first flush standpipe (with a valve and bottom cleanout). As the water rushes off the roof, it goes into the vertical stand pipe. When the vertical pipe is filled, the water than goes into the horizontal pipe and begins filling the storage tank. After the rain stops, the standpipe is drained in preparation for the next rain.

## Slide 18
Pump and Pressure Tank
Notes: If a system if not gravity-fed, an electric pump may be needed. If you are using the harvested water for household use, a pressure tank likely will be needed. This would assist with the distribution of the water.

## Slide 19
Filters and Sanitizers – Drinking H2O
Notes: Filters and sanitizers are necessary if the water is to be used as the source of drinking water. Roofwashing, filters, and continuous disinfection help to assure safe water for human consumption.. Most common methods used to disinfect the water are ultraviolet light or chemical disinfection.

## Slide 20
Drip irrigation – Landscape or Garden
Water garden in ground
Wildlife and pet water
Sprinklers, misters & watering with pressure
In home uses
Distribute Water to Desired Location

## Slide 21
Rainwater can be used in a water feature with floats that keep the water level high enough to run reciprocating pumps.
Water Features in Landscape

## Slide 22: Rainwater Harvesting
Rainwater harvesting captures, diverts and stores rainwater for later use.
Easiest use is for landscaping irrigation
Can be used for household use with proper treatment.
Rainwater is good for plants because it is free of salts and other minerals

## Slide 23: Rainwater Harvesting
Reduces the demand for chlorinated or other chemically treated tap water therefore you buy less water
Reduces the amount of water that will go into storm sewers where it is mixed with oil and other toxic residues from streets, parking lots etc.

## Slide 24: Resources
Rainwater Harvesting – B-6153 Texas AgriLife Extension Service, TAMUS
http://agrilifebookstore.org/publications_details.cfm?
whichpublication=1979 $4.50
Texas Guide to Rainwater Harvesting, Texas Water Development Board
http://www.twdb.state.tx.us/assistance/conservation/Alternative_Technologies/Rainwater_Harvesting/Rain.asp

## Slide 26
Billy Kniffen
CEA-AG
Menard, Texas 76859
325-393-2120
e-mail:
b-kniffen@tamu.edu
Special Thanks to: